## Slide 1
H-SIM
Himalayan Slope Instability Model
Notes: H-SIM answers one question for the selected countries — India, Nepal and Bhutan in the shipped config, all eight HKH members one setting away: of all the places people and roads sit under Himalayan slopes, which deserve attention first? One physically based model, one product, honestly labelled. The tagline is the app's legend: colour encodes exposure, the stroke pattern encodes how a road fails.

## Slide 2
H-SIM Regional Coverage
Failure probability, exposed settlements and exposed road segments for every mountain province — ranked, mapped, and browsable from a single web app that runs from a folder. No server, no login.
45
states & provinces: India · Nepal · Bhutan
3
countries selected — widens to all 8 HKH
90 m
grid, regionally; 30 m for calibration
2021–60
both near-term CMIP6 windows, run in full
Notes: For management: the deliverable is one HTML file that opens in any browser. 45 provinces ranked by how much of their ground the model calls unstable, with the human stakes beside each. Selecting a province embeds its full map. Everything else in this deck explains why those numbers can be trusted, and exactly how far.

## Slide 3
The physics: SINMAP over real drainage
water table (steady-state recharge)
soil surface — column depth h
θ
FS = resisting / driving — cohesion + friction vs gravity, weakened by wetness
w = min( R·a / (T·sinθ), 1 ) — wetness from the D∞ contributing area
1
Infinite-slope stability
Shallow translational failure on a planar slip surface — the mechanism behind most rainfall-triggered Himalayan slides.
2
Steady-state hydrology
Wettest-month recharge routed over D-infinity flow directions: hollows that concentrate water concentrate failure.
3
Monte Carlo over fitted ranges
Soil parameters are uncertain, so they are ranges fitted to mapped landslides; the output is the probability FS < 1.
Notes: For engineers: SINMAP closes the infinite-slope equation with a steady-state wetness term. Pseudo-static seismic loading extends it to earthquake scenarios; CMIP6 recharge scaling extends it to 2060. The honest part: parameters are fitted ranges, not lab values, and the map is the probability over those ranges — relative by construction.

## Slide 4
From data to deliverable: ten resumable steps
1–2
Check &
download
3
Calibrate
(Gorkha, 30 m)
4
Validate
transfer
5
Sweep the
provinces
6
Climate
scenarios
7–8
Settlements
& roads
9
Web app
10
Package
Built for interruption
A regional pass at 90 m takes days; every stage resumes, and a province with output is skipped.
Provinces are routed on a buffered box and clipped back — border catchments stay intact (measured: 0.00% distortion at a 3 km buffer).
province-refresh is deadline mode: worst provinces first, the app rebuilt after every one — presentable at any moment. --rebuild-pages rolls a page redesign across a finished region in seconds per province.
Notes: Each numbered step is one CLI command; the README's Quick Reference lists them in order. The design assumption is that something always interrupts a multi-day sweep, so resumability is a first-class feature, and cheap refresh paths exist for display-only changes.

## Slide 5
Evidence, not vibes: measured skill
Chart: Resolution dominates everything else
| 250 m | 90 m | 30 m
Spatial-block CV AUC | 0.7281 | 0.8059 | 0.8156
0.816 AUC
held-out, spatial-block CV on the Gorkha inventory at 30 m; 71% of slides captured in the worst-ranked 20% of terrain.
0.780 → 0.656
transfer without refitting: Sikkim, then monsoon-driven Far-West Nepal, 400 km from the fit. Measured, not assumed.
0.472 AUC
Shimla road-cut failures — worse than chance. Published as a limit, and the reason road mechanisms are flagged, not scored.
Notes: Every claim traces to a script in analysis/ and a JSON of results. The failure case is presented with the successes: on Shimla's road-cut inventory the model inverts, which is why the app never pretends to score cut-slopes — it flags them as geometry instead.

## Slide 6
Exposure done right: what each asset now carries
◑
Clipped to the province
Settlements and roads outside the boundary are a neighbour's; they are dropped from scores, maps and counts — nothing is counted twice.
●
Footprints, not centroids
A town is scored over a disc scaled to its type and headlined at the 90th-percentile cell: the exposed edge, not the safe centre.
➤
The threat has a direction
Each asset reports the compass sector its worst weighted sources sit in — 'from the NE' is something a field visit can walk.
▦
Supply, not just fraction
Expected unstable area positioned to reach the asset (hectares): thirty source cells stop looking like three thousand.
Notes: Four upgrades to how assets are scored, all visible in the app's popups. The clip fixed a real defect — Meghalaya's map used to show Bangladeshi villages floating outside the border. Footprints, sector and supply are literature-grounded: GHS-BUILT can replace the disc radii behind the same interface when we add the dataset.

## Slide 7
Roads fail three ways — the line style says which
Burial from above
The reach score: unstable ground positioned to deliver onto the road. This is the coloured line itself.
scored by the model
Cut-slope
Steep ground immediately above the segment. The model measurably cannot score road cuts (Shimla), so this marks its blind spot.
geometric flag — >35° adjacent
Washout
The segment touches a mapped channel. Culverts are taken by debris flows arriving along the drainage, from beyond any search radius.
geometric flag — SCA > 5,000 m
On the map: the stroke pattern names the mechanism — solid burial only, dashed cut-slope, dotted washout, dash-dot both — under a dark casing that appears as you zoom in; colour stays the segment's exposure. A red dotted line is a crossing fed by ground the model calls unstable.
Notes: This is the display rule the whole app teaches: colour = exposure, line style = mechanism. Two of the three mechanisms are honest geometric flags rather than model output, and the app's legend says so — that honesty is what makes the map defensible in front of a road department.

## Slide 8
Discipline: features ship OFF until a number says yes
Precedent: per-lithology calibration was physically plausible — and measured at –0.0004 held-out AUC. It ships off. Every refinement since inherits that bar.
Flow-connectivity reach weighting
Debris paths follow drainage (Flow-R; Horton 2013). Sources are re-weighted by the fraction of their D∞ flow routed through the asset.
analysis/08_connectivity.py — polygon runout toes vs background, cone vs connectivity, adopt only if the AUC gain beats the resampling noise.
Slope-dependent soil depth
Regolith thins as slopes steepen (DeRose 1996). One factor scales cohesion and R/T together; the fit grid grows 48 → 144 candidates.
analysis/09_soil_depth.py — same folds as the lithology test; adopt only if held-out AUC improves in both areas and nonzero depth is actually chosen.
Notes: Both features are fully implemented, unit-tested on constructed terrain, and OFF. The experiment scripts are the switches; each prints an explicit ADOPT or NULL verdict. This is the repository's core epistemics: physically motivated is not the same as measurably better.

## Slide 9
The app: one page drives the whole region
Himalayan Slope Instability Model
Country ▾
Province ▾
embedded province map
tabs: Map · Provinces table · Glossary — click anything for its explainer
Management
The ranked table is the agenda: which provinces, how much exposed, and how many distinct risk clusters — settlement and road — each holds.
Technical teams
Scenario selector re-plays the same terrain under storms, shaking and CMIP6 futures; the sidebar recomputes live.
Engineers
Popups carry the full record — score, terms, worst source, a compass arrow for the threat sector, supply, mechanism patterns — and green/yellow cluster shapes sit in the layer picker.
Notes: The same page serves three audiences. Every card, column and control opens its own explainer on click, and a Glossary tab plus each province's sidebar glossary state every definition — including, for every percentage, what it is a percentage of. Colour is exposure, line style is mechanism, scenarios re-play the terrain. Works offline from a folder; a MapTiler key upgrades the basemap, a keyless CARTO fallback keeps it working without one.

## Slide 10
Say these out loud before presenting the maps
Relative, not absolute
Differences between places are meaningful; the value is not an annual probability of failure.
Screening, not risk
Angle-of-reach exposure — no runout model, no vulnerability, no damage function. Stated in the methods and the app's glossary.
Skill is measured where inventories exist
All three inventories sit in the eastern half; westward the skill is unknown rather than assumed.
Shallow failures only
Deep-seated slides, rock avalanches and road-cut collapses are outside the physics — the last is flagged, never scored.
Notes: These four sentences are the difference between a defensible screen and an over-claim. They appear in the README, in METHODS.md, in the app's glossary and in every summary JSON's note field.

## Slide 11
Running it: the whole product in six commands
pytest tests/ -q # 110 tests, seconds
h-sim step3-calibrate --config configs/01_gorkha_calibration.json
h-sim step4-validate --config configs/01_gorkha_calibration.json
h-sim step5-susceptibility --config configs/02_hkh_region.json # days
h-sim province-refresh --config configs/02_hkh_region.json # worst first
open outputs/hkh_region/index.html # the deliverable
Everything resumes, and only what a marker failed to produce re-runs. province-refresh grows the app one finished province at a time; --rebuild-pages re-skins a finished region in seconds per province; prune-excluded reclaims disk from deselected countries.
Notes: Operationally simple by design: one config file per product, one command per stage, resumable everywhere. The 'h-sim' shorthand stands for 'python -m h_sim.cli'.

## Slide 12
What earns its way in next
Run the two switches on real inventories: analysis/08 (connectivity), analysis/09 (soil depth) — adopt on ADOPT, record on NULL.
GHS-BUILT built-up extent to replace footprint discs, behind the same interface.
Network criticality for roads — which cut actually severs a valley — as its own project.
github.com/ntwarakavi/Himalayas_LandslideRisk
Notes: The roadmap follows the same rule as everything shipped: implemented, tested, and gated on a held-out number. Questions welcome — every figure in this deck traces to a script and a results JSON in the repository.